## Slide 1
GEO 391 – Machine Learning Applications in Geoscience
Spring 2022
CNN-RNN Forward Proxy Modeling for CO2 monitoring
Team MOMA: Misael Morales & Oriyomi Raheem

## Slide 2: Contents
Problem statement
Reservoir Simulation
Data Processing
CNN-RNN Proxy Model
Training & Testing
Results, Discussion & Conclusion
2

## Slide 3: Problem statement
Question, Problem, and Proposal
3

## Slide 4: Problem Statement
Reservoir simulation is crucial for subsurface energy resource engineering
  Often, it is very complex and time-consuming
Develop a deep learning framework for forward reservoir simulation
  Better computational efficiency
  Accuracy trade-off
Exploit latent space dynamics for timelapse predictions using CNN-RNN architecture
4

## Slide 5: Problem Statement
Numerical Simulation
(MRST)
Reservoir Model
(SPE10)
Data Processing
(Python)
Deep Learning
(Keras)
1 injector
CO2
years injection, monitor monthly
Tarbert (Gaussian) + Ness (fluvial)
Reshape to images
Data augmentation (rotation)
Random Shuffling
Min-Max Normalization
Train/Test split
Two-phase water-gas model
FD + Automatic Differentiation
Output: dynamic pressure & saturation fields
&
Encoder: Conv2D
Recurrent: GRU
Decoder: Conv3DTranspose
Compile, Fit & Predict
5

## Slide 6: Problem Statement
6
SPE10 model
partition
grid
reservoir
simulation
ML
proxy
CNN-RNN proxy to exploit latent space dynamics

## Slide 7: Reservoir Simulation
Model construction and computation
7

## Slide 8: Reservoir Simulation
Inputs
Grid
Rock properties
Fluid properties
Initial state
Wells
Boundary conditions
Schedule
Solver
8
Outputs
Numerical report
Well solution
Pressure states
Saturation states
y
x

## Slide 9: Reservoir Simulation
High-fidelity simulations are performed using MRST
255, 2D realizations with 1 injector
  Initially water saturated
  CO2 injection @ 5 m3/day
  5 years, monitored monthly
  Automatic Differentiation framework
Parallelized over 10 cores on an Intel i9-10900K @ 5000 MHz
  seconds per realization
9

## Slide 10: Data Processing
Preparing data for deep learning
10

## Slide 11: Data Processing
HFS results are sliced to: and
  Exported as MATLAB (*.m) files
  Imported using SciPy
Reshape to 2D images and 3D “videos”
Data augmentation by rotation
Shuffle concatenated dataset
  Make proxy agnostic to orientation, learn true flow physics
11

## Slide 12: Data Processing
12
y
x

## Slide 13: Data Processing
Min-Max Normalization
  For each realization & for each state:
Train/Test split
  Randomly assigned train/test index
13

## Slide 14: CNN-RNN Proxy model
Convolution & Recurrent layers, Latent space representations, and Model building
14

## Slide 15: CNN-RNN Proxy Model
The convolutional layer
The recurrent layer
Return sequence = True
15

## Slide 16: CNN-RNN Proxy Model
Dynamic output
Static input
RNN block
Total # of Parameters:
16

## Slide 17: CNN-RNN Proxy Model
The Encoder
Conv2D
Conv2D
BatchNorm
LeakyReLU
MaxPool2D
regularization
LeakyReLU activation
Convolutional block
Conv Block 1
Conv Block 2
Conv Block 3
Conv Block 4
17

## Slide 18: CNN-RNN Proxy Model
The Recurrent block
RepeatVector
Reshape
Flatten
GRU
Flatten
RepeatVector
GRU
Reshape
Recurrent block
18

## Slide 19: CNN-RNN Proxy Model
The Decoder
ConvT3D
ConvT3D
BatchNorm
LeakyReLU
regularization
LeakyReLU activation
Transpose Convolutional block
ConvT3D
ConvT Block 1
ConvT Block 2
ConvT Block 3
Output Block
ConvT3D
Conv3D
19

## Slide 20: Training & testing
Performance and Visualization
20

## Slide 21: Training & Testing
Compile
  Optimizer = Nadam (Adam with Nesterov momentum)
  Loss = MSE
Fit
  Epochs = 300
  Batch size = 40
  Validation split = 0.25
  Workers = 10
minutes on Nvidia RTX 3080
21

## Slide 22: Training & Testing
Use trained model to show training predictions
  MSE = 0.016 ; SSIM = 0.817
22

## Slide 23: Training & Testing
Testing predictions
  MSE = 0.040 ; SSIM = 0.563
23

## Slide 24: Results, Discussion & Conclusions
Lessons Learned, Possible Applications, and Future Directions
24

## Slide 25: Results, Discussion & Conclusions
High-Fidelity Simulations
  Crucial yet costly step in reservoir characterization and forecasting
  HFS performed in MRST from SPE10 partition
  Approximately 20 seconds per realizations
Data Processing
  Data: feature (static – permeability) & target (dynamic – saturation)
  Augmentation by rotation; Random shuffling; Min-Max Normalization; Train/Test split
  Optimized for use in Keras deep learning framework to make proxy model learn the physics of the system
25

## Slide 26: Results, Discussion & Conclusions
Proxy Model
  Block architecture: Encoder – Recurrent – Decoder
  Approximately 930,000 parameters
  Each prediction is milliseconds x speedup!
Results
  The proxy model is extremely efficient in predicting dynamic saturation states from a static permeability map.
  Train MSE, SSIM = 0.016, 0.817
  Test MSE, SSIM = 0.040, 0.563
26

## Slide 27: Results, Discussion & Conclusions
Conclusion
  Including a SSIM loss function to improve testing predictions
  Expand training data through augmentation or generate more realizations
  Applications:
    Uncertainty quantification
    History matching / parameter estimation / model calibration
    Closed-loop optimization
  Other areas:
    Groundwater flows
    Contaminant transport
    Petroleum production
27

## Slide 28: References
Maldonado-Cruz, Eduardo, and Michael J Pyrcz. (2022) “Fast Evaluation of Pressure and Saturation Predictions with a Deep Learning Surrogate Flow Model.” Journal of petroleum science & engineering 212
Kim, Y. D., & Durlofsky, L. J. (2022). "Convolutional-Recurrent Neural Network Proxy for Robust Optimization and Closed-Loop Reservoir Management." arXiv preprint arXiv:2203.07524.
Kaur, Harpreet et al. (2022) “Time-Lapse Seismic Data Inversion for Estimating Reservoir Parameters Using Deep Learning.” Interpretation (Tulsa) 10.1
S. Pan, S.L. Brunton, and J.N. Kutz (2022) "Neural Implicit Flow: a mesh-agnostic dimensionality reduction paradigm of spatio-temporal data." arXiv preprint arXiv:2204.03216
Joon, Shams, Dawuda, Ismael, Morgan, Eugene, and Sanjay Srinivasan. (2022) "Rock Physics-Based Data Assimilation of Integrated Continuous Active-Source Seismic and Pressure Monitoring Data during Geological Carbon Storage." SPE Journal.
Gonzalez, Keyla, and Siddharth Misra. (2022) “Unsupervised Learning Monitors the Carbon-Dioxide Plume in the Subsurface Carbon Storage Reservoir.” Expert systems with applications 201
K.G. Gurjao, E. Gildin, R. Gibson, and M. Everett. (2022) "Estimation of Far-Field Fiber Optics Distributed Acoustic Sensing DAS Response Using Spatio-Temporal Machine Learning Schemes and Improvement of Hydraulic Fracture Geometric Characterization." SPE Hydraulic Fracturing Technology Conference and Exhibition, USA
Salazar, Jose J et al. (2022) “Fair Train-Test Split in Machine Learning: Mitigating Spatial Autocorrelation for Improved Prediction Accuracy.” Journal of petroleum science & engineering 209:109885–.
Tang, Meng, Yimin Liu, and Louis J Durlofsky. (2021) “Deep-Learning-Based Surrogate Flow Modeling and Geological Parameterization for Data Assimilation in 3D Subsurface Flow.” Computer methods in applied mechanics and engineering 376:113636–.
H. Jo, Y. Cho, M.J. Pyrcz, H. Tang, and P. Fu (2021) "Machine learning-based porosity estimation from spectral decomposed siesmic data." arXiv preprint arXiv:2111.13581
Wen, Gege, Catherine Hay, and Sally M Benson. (2021) “CCSNet: A Deep Learning Modeling Suite for CO2 Storage.” Advances in water resources 155:104009–.
Alsulaimani, Thamer , and Mary Wheeler. (2021) "Reduced-Order Modeling for Multiphase Flow Using a Physics-Based Deep Learning." SPE Reservoir Simulation Conference
E.J.R. Coutinho, M.J. Aqua and E. Gildin. (2021) "Physics-Aware Deep-Learning-Based Proxy Reservoir Simulation Model Equipped with State and Well Output Prediction." SPE Reservoir Simulation Conference, Virtual.
Ciriello, V., Lee, J. & Tartakovsky, D.M. (2021) "Advances in uncertainty quantification for water resources applications." Stoch Environ Res Risk Assess 35, 955–957
Pan, W., Torres-Verdín, C. & Pyrcz, M.J. (2021) "Stochastic Pix2pix: A New Machine Learning Method for Geophysical and Well Conditioning of Rule-Based Channel Reservoir Models." Nat Resour Res 30, 1319–1345
Wu, Hao et al. (2021) “A Multi-Dimensional Parametric Study of Variability in Multi-Phase Flow Dynamics During Geologic CO2 Sequestration Accelerated with Machine Learning.” Applied energy 287:116580–.
Santos, J.E., Yin, Y., Jo, H. et al. (2021) "Computationally Efficient Multiscale Neural Networks Applied to Fluid Flow in Complex 3D Porous Media." Transp Porous Med 140, 241–272
Chan, S., Elsheikh, A.H. (2020) "Data-driven acceleration of multiscale methods for uncertainty quantification: application in transient multiphase flow in porous media." Int J Geomath 11,3
Cheung, S.W., Chung, E.T., Efendiev, Y. et al. (2020) "Deep global model reduction learning in porous media flow simulation." Comput Geosci 24, 261–274
Almasov, Azad , Onur, Mustafa , and Albert C. Reynolds. (2020) "Production Optimization of the CO2 Huff-N-Puff Process in an Unconventional Reservoir Using a Machine Learning Based Proxy." SPE Improved Oil Recovery Conference, Virtual
Jiang, Chiyu lmaxr et al. (2020) “MESHFREEFLOWNET: A Physics-Constrained Deep Continuous Space-Time Super-Resolution Framework.” SC20: International Conference for High Performance Computing, Networking, Storage and Analysis. IEEE 1–15.
J. Nagoor Kani, Elsheikh, A.H. (2019) "Reduced-Order Modeling of Subsurface Multi-phase Flow Models Using Deep Residual Recurrent Neural Networks." Transp Porous Med 126, 713–741
Jayne, Richard S, Hao Wu, and Ryan M Pollyea. (2019) “Geologic CO2 Sequestration and Permeability Uncertainty in a Highly Heterogeneous Reservoir.” International journal of greenhouse gas control 83.C:128–139.
K.-A. Lie. (2019) "An Introduction to Reservoir Simulation Using MATLAB/GNU Octave: User Guide for the MATLAB Reservoir Simulation Toolbox (MRST)." Cambridge University Press
Brunton, Steven L., and Jose Nathan Kutz. (2019) "Data-Driven Science and Engineering: Machine Learning, Dynamical Systems, and Control." 1st ed. Cambridge University Press
Guo, Zhenyu, and Albert C Reynolds. (2018) “Robust Life-Cycle Production Optimization With a Support-Vector-Regression Proxy.” SPE journal 23.6:2409–2427
Naraghi, Morteza Elahi, Spikes, Kyle , and Sanjay Srinivasan. (2017) "3D Reconstruction of Porous Media From a 2D Section and Comparisons of Transport and Elastic Properties." SPE Res Eval & Eng 20:342–352
Ampomah, W et al. (2017) “Optimum Design of CO2 Storage and Oil Recovery Under Geological Uncertainty.” Applied energy 195
J. Nagoor Kani, Elsheikh, A.H. (2017) "DR-RNN: A deep residual recurrent neural network for model reduction." arXiv preprint arXiv:1709.00939
28

## Slide 29: Thank you!
Questions?
Misael Morales:
PhD Student in Petroleum & Geosystems Engineering
Advisors: Dr. Michael Pyrcz, Dr. Carlos Torres-Verdin
GitHub | Linkedin | Website | misaelmorales@utexas.edu
Oriyomi Raheem:
PhD Student in Petroleum & Geosystems Engineering
Advisor: Dr. Carlos Torres-Verdin
oriyomiraheem@utexas.edu
Link to notebook:
https://github.com/misaelmmorales/CNN-RNN-CO2
29

## Slide 30: Backup slides
30

## Slide 31: Simulation Variables
Reference pressure: mega Pascals
Reference temperature:
Water compressibility:
Rock compressibility: bars
Water viscosity: Pascal-second
CO2 viscosity: Pascal-second
Residual water saturation:
Residual CO2 saturation:
Water viscosity: 1000
31

## Slide 32: Simulation Variables (continued)
Grid size: 60x60x1
Grid dimensions: 20x10x5 ft
Initial reservoir pressure: psia
Initial reservoir saturation: -
Total simulation time: 5 years
Monitor steps: 1 month
Total steps: 60
Wellbore radius: 0.05
AD Solver: TwoPhaseWaterGasModel
32

## Slide 33: Proxy Model Variables
L2 regularization: 1e-4
LeakyReLU alpha: 0.3
RNN dropout: 0.2
Nadam learning rate: 5e-4
33